## Slide 1
Data Mining and Machine Learning Tools for Combinatorial Material Science of All-Oxide Photovoltaic Cells
Abraham Yosipof,* Assaf Y. Anderson, Hannah Noa Barad, Sven Rühle, Arie Zaban and Hanoch Senderowitz
Department of Chemistry, Center for Nanotechnology & Advanced Materials, Bar Ilan University, 52900 Ramat Gan, Israel
*e-mail address: avi.yosipof@gmail.com
ABSTRACT
Recently a new field in photovoltaics (PV) is emerging focusing on solar cells that are entirely based on metal oxide (MO) semiconductors. All-Oxide based photovoltaics have the potential for extremely low cost solar cells, provided they can show an order of magnitude improvement in their power conversion efficiencies. The development of such cells could benefit from combining combinatorial material sciences of compounds with data mining and machine learning tools to analyze and rationalize the empirical results and for the design of new compounds.
Here we describe what we believe to be the first reported application of data mining and machine learning techniques in the field of photovoltaics. To establish the tools in this new field, we focused on a library of 169 solar cells of TiO2/CuO. Each cell was characterized by 7 independent variables (i.e., descriptors) and by 3 dependent variables (photovoltaic parameters). Following characterization, cells were divided into training and test sets using a newly developed representativeness function. Individual models were derived for all independent variables with various techniques leading to good models with R2CV and R2Test typically > 0.8. For the open circuit photovoltage (VOC), no models could be derived presumably due to the presence of outliers. Ten outliers were removed using an in-house developed outlier removal algorithm and the remaining compounds were re-subjected to the model building procedures yielding this time reliable models. In summary we have demonstrated the usefulness of data mining and machine learning tools in the field of photovoltaics.
Model Building and Validation
k-Nearest Neighbors optimization models
Genetic Programing models
Experimental Data
Solar cells library of TiO2/CuO
library
(a) Transparent conducting oxide (TCO)
coated glass
(b) Sprayed TiO2 layer
(c) Pulsed Laser Deposition (PLD) of Cu–O
(d) Round Ag back contacts sputtered
on top of the Cu–O layer
Experimental Data collection
Calculated Internal Quantum Efficiency (IQE) as a function of cell position
Library Characterization
Dependent variable Y: Photovoltaic parameters
  Jsc: The short circuit photocurrent
  VOC: The open circuit photovoltage
  IQE: The internal quantum efficiency
Independent variable X: Cells characterization
  d_ TiO2: The thickness of the TiO2 layer
  d_ CuO: The thickness of the CuO layer
  Ratio: The thickness ratio between the two layers
  d_c [CuO]_plume: The distance of the cell from the center of the CuO depositing plume
  BGP: The band gap of the CuO
  Ex situ R : The resistance of the CuO
  Max_J: The maximum calculated photocurrent
Workflow
Model Building: Spilt Data
Representativeness optimization algorithm to split the data for Training set and Validation test set.
Minimize Representativeness function subset through MC
Randomly select a subset of Cells
Calculate distances between dataset and subset
f(distance between dataset & subset)
Select most representative subset
Input: Cells and descriptors
Data Visualization
Principal Components Analysis (PCA)
    Reduce dimensions for visualization
    Deduct outliers
Chart: PC1
Model Building: kNN optimization based outlier removal
For VOC no model was obtained for the entire library
Outliers removed using a new kNN-based algorithm
The improvement of the VOC model in each cycle
Remove that cell which provides the largest increase in R2cv upon its removal from the dataset
Dataset
For each cell, calculate the improvement in R2cv upon its removal from the dataset
Stopping criteria: model with R2cv >0.9
Run kNN optimization to obtain the best model
Calculated Internal Quantum Efficiency (IQE) as a function of cell position